Aerosol Users Manual

---
Abstract
- AEROSOL is a general purpose code for solving the conservation equations of a spatially homogeneous single chemical component aerosol
- The mechanisms which may be incorporate to determine the evolving particle size distribution are:
  1. Coagulation
  2. Deposition
  3. Aerosol generation
  4. Nucleation
  5. Particle growth by condensation
A new code will be available which not only computes the particle size distribution, but also the distribution of chemical species with respect to particle size, the new code is called MAEROS, which is significantly smaller and faster the AEROSOL, is based on work reported in references (7) and (8) of this manual

---
Introduction
- AEROSOL program: simulate the size distribution dynamics of a spatially homogeneous aerosol
- The program is general purpose code for solving population balance equations and is there for not restricted to only aerosol problems
- It is assumed that the user is familiar with derivation of population balance equations (General dynamic equation(GED)), the details and numerics have been omitted
- This manual is divided into 7 parts:
  - Section 1: introduction
  - Section 2: forms of the GDE that can be solved by AEROSOL is given
  - Section 3: numerical techniques
  - Section 4: five types of subroutines
  - Section 5: proper format for input data
  - Section 6: array dimensions for altering storage requirements
  - Section 7: nine example problems

---
Procedure of aerosol
- Read each case from IN.DAT and compute each case
- Read and check input data,
  - error is found(ISTOP=1), skip the case, no errors(ISTOP=0)
  - call SETUP if needed for interpolation and continue
Check for negative values of the distribution,
  - if a negative value was found and grid points were added(ISTOP=-1), recheck the interpolation scheme
  - if a negative value was found and no grid points were added(ISTOP=1) skip the case
- Now that the input data and distribution have been checked, output the initial conditions and initialize output counters (ie. IPTIM and JPRTIM), and the flag for the O.D.E. package(ie. IODEPK).
- Compute the solution of the case for NPRNT output times
- If grid points have been added(ie, ISTOP=-1), restart calculation and try again to reach TOUT(JPRTIM). If the distribution is negative and no grid points have been added(ie, ISTOP=1), skip to the next case
- Check if the spline interpolation method is to be changed or if the steady state approximation is to be used for the discrete regime
- Print error message and proceed to next case

---
Section 2: General Dynamic Equation

---
Discrete general dynamics equation
- In the most fundamental form of the GED, particles are represented as consisting of integer multiples of a single structural unit, typically a molecule
- In discrete equation, particles differ only in the number of monomers they contains
- A spatially homogeneous aerosol, the concentration of monomers is governed by
- Where
{dN} over {dt}=- N_{l} sum from{j=1} to {infinity } { %beta_{l,j} } { N_{j} } + { N_{i}}sum from{ j=1 } to { infinity } ({ 1+ %delta_{2,j} }) {E_{j}}{ N_{j} }+ overline {S_{l}}( t )+overline{ R_{l} }( N_{l},t )
{ %delta_{2,j} }= left lbrace (0 j<>2), (1 j=2) right rbrace

---
Discrete-Continuous general dynamics equation
- When the size of particle is small, the growth of its size is discrete
- For large particles, the difference in size between an i-mer and (i+1)-mer is relatively small, the growth of its size can be viewed as continuous
- Approximate continuous regime to discrete, because the range of integration is so small
N_{ i } = int from{x_{i}} to{x_{i}+x_{l}} n( x,t )dx
n( x_{i},t )= N_{ i } over x_{ l },i>k

---
Continuous general dynamics equation
So we can just divide the particle size domain into a step function
dN_{ l } over dt =-N_{ l } [ sum from{j=1} to {k} %beta_{1,j}N_{j}+ int from{x_{k+1}} to{infinity} %beta(x_{l},y)n(y,t)dy]+ sum from{ j=2 } to{ k }( 1+%delta_{2,j}E_{j}N_{j} ) + int from{ x_{k+1} } to{ infinity }E( y )n( y,t )dy+ overline {S_{l}}( t )+overline{ R_{l} }( N_{l},t )

---
Section 3: Numerical Techniques

---
3.1 continuous regime
- n(x,t) is assumed to a continuous function of x
- By determining the temporal variations of n(x,t) at a finite number of grid points in x, the values of n(x,t) at intermediate points can be determined by interpolation
- Because x typically varies over many orders of magnitude, the following logarithmic rescaling is used in the code:
w={ ln(x over x_{a}) } over { ln(x_{b} over x_{a}) }

---
w={ ln(x / x_{a}) } over { ln(x_{b} / x_{a}) }
- Xa: lower mass limits
- Xb: upper mass limits
- Supply three options of interpolation formulas:
  - Cubic
  - Linear
  - Logarithmic spline
- DISTW, SETUP and DERIVT determine the interpolation formula

---
Cubic interpolation code
double CubicInterpolate( double y0,double y1, double y2,double y3, double mu)
{
double a0,a1,a2,a3,mu2;
mu2 = mu*mu;
a0 = y3 - y2 - y0 + y1;
a1 = y0 - y1 - a0;
a2 = y2 - y0;
a3 = y1;
return(a0*mu*mu2+a1*mu2+a2*mu+a3);
}

---
Cubic interpolation
- If the values of a function f(x) and its derivative are known at x=0 and x=1, then the function can be interpolated on the interval [0,1] using a third degree polynomial
- Require four points and two of them on either side
- mu behaves the interpolation between the segment y1 to y2.

---
Linear interpolation
- If the two known points are given by the coordinates and , the linear interpolation is the straight line between these points. For a value x in the interval , the value y along the straight line is given from the equation
( x_{0},y_{0} )
( x_{1},y_{1} )
( x_{0},x_{1} )
{y-y_{ 0 }}over{ x-x_{0} }= { y_{1}-y_{0} } over { x_{1}-x{0} } drarrow y=y_{ 0 } +( y_{1}-y_{0} ){ x-x_{0} }over{ x_{1}-x_{0} }

---
Linear interpolation code
float linearInterpolation(
float x0, float yo,
float x1, float y1, float x)
{
return y0 + (x-x0)*(y1-y0)/(x1-x0);
}

---
Logarithmic interpolation
- If the axis is not on a linear scale but rather on a logarithmic scale, we can utilize logarithmic interpolation to simplify the problem.
- Like what has introduced.

---
DISTW(ISPLIN,NVARM1,NPTS,ZDIST)
- This function computes the values of the M(WX,T) distribution by interpolating from the values of A at the grid points.
- According to the input flag to determine the interpolation method.

---
3.2 Discrete regime
- In discrete regime is governed by solving a set of k ordinary differential equations.
- Specify the number of discrete sizes, the code will determined all the cluster sizes and the smallest particle size in the continuous regime
- One must specify grid point locations in the continuous regime in the range
N_{ i } ( i=1...k )
x_{ k+1 } leslant x leslant x_{ 2k }

---
Assume the concentration of molecular clusters has reached steady state:
  1. Doing
  2. Using
  3. Doing
  4. initially

---
3.3 Temporal integration
The temporal variations of n(x,t) at the grid points and are governed by a set of first order ordinary differential equations.
N_{ i } ( i=1...k )

---
3.4 Integrations with respect to particle size
Gaussian-Legendre quadrature is used to evaluate the coagulation integrals over particle size (4)

---
3.5 Units for dimensional quantities
The coefficients and initial distribution are supplied by the user, they may be dimensionless or in any consistent set of units

---
3.6 possible numerical difficulties
- Two situations which may cause some difficulty
- This “finite domain error” must be distinguished from errors usually associated with numerical solutions
- The second problem that the user may encounter involves interpolation of the distribution.
  - An inaccurate formula
  - A high order formula may be smoother than a low order formula but more likely to yield negative values in regions where the distribution varies rapidly with particle size.

---
Section 4: Subroutines

---
20 routines and 4 categories in AEROSOL
- First category: specify the kinetic coefficients and initial conditions
  - Define the problem
- Second category: determine the interpolation and integration method, and the form of output
- Third category: 4 routines
  - Diagnose user input for possible errors or inconsistencies
  - Check the interpolation method and add grid points as needed
  - Compute variation in the first moment of the distribution
  - Compute the steady state approximate solution for the discrete regime
  - Errors are easy to be neglected in these subroutines
Fourth category: control the code by reading the input data, calculating coefficients, storing the values of kinetic coefficients and providing the derivatives needed for the O.D.E. package

---
Coefficients specification routines

---
BETA(NPTS,TIME,X,YARRAY,COEF)
The routine calculates NPTS coagulation coefficients for two particles of sizes X and YARRAY(I), I=1,...,NPTS, at time TIME
  - NPTS: the number of points
- The coefficient for a particle of size X and that of size YARRAY(I) are stored in COEF(I)
- NPTS(number points) is an integer and TIME, X, YARRAY and COEF are real variables
- YARRAY and COEF must be dimensioned to 1//array
- COEF must be positive and symmetric with respect to the sizes of the coagulating particles,
  - it is better to use a time dependent coefficient
  - an improper coefficient will result in error message
- TIME is in seconds
- X and YARRAY are in cubic centimeters//volumn
- COEF is in cubic centimeters per second
- User may pass 10 integer values to any subroutine through the common blck AERSL1
- The third integer of the common block AERSL1 is used to determine which function will be used for the coagulation coefficient.
- no implementation

---
BOUNDR(TIME)
- If condensation is included in the continuous GDE, particles in the range about xa are often assumed to be forming due to nucleation.
- The BOUNDR function enables the user to specify the source rate at x=xa as a function of time.
- AERSL 6 is used to access the output times, TOUT(I) to modify BOUNDR past the second output time.
- This routine is used only if condensation is requested.
- No implementation

---
CSOURC(NPTS, TIME, X, DISTX, SOURCE, REMOVE)
- This routine calculates the continuous source function and the continuous removal function
- Two-dimensional array: SOURCE and REMOVE
- The first subscript of SOURCE or REMOVE corresponds to the specific source or removal mechanism respectively
- The second subscript corresponds to the points in the X array
- More information about this subroutine is in Figure 3

---
DSOURC(NPTS, TIME, CLSCON, SOURCE, REMOVE)
- This routine is the discrete analogue of CSOURC, calculating the discrete source function and the discrete removal function
- The first subscript of SOURCE or REMOVE corresponds to the specific source or removal mechanism respectively
- The second subscript corresponds to the cluster size.
- A list of the DSOURC routine supplied with the code is given in Figure 4

---
EVAP(NPTS, TIME, X, COEF)
- This routine calculates the evaporation coefficient E(xi), at xi=X(I), i=1...NPTS at time TIME and stores the result in COEF(i)
- A listing of the EVAP routine supplied with the code is given in figure 5.
- The first integer of the common block AERSL1 is used to determine if evaporation is to be included in the simulation.
- EVAP uses the BETA routine
- This routine is used only if the discrete-continuous GDE is requested and the user has the option of using a time dependent evaporation coefficient.

---
GROWTH(NPTS, TIME, X, RATE, PARTAL)
- This subroutine calculates the growth rate, the partial of the growth rate with respect to particle size, and store the result in RATE(I) and PARTAL(I) respectively.
- A listing of the GROWTH routine supplied with the code is given in figure 6
- Notice from figure 6 that the third integer in the common block AERSL1 is used to determine the functional form of RATE.
- For IPARAM(3) equal to 1, an illegal growth rate will be computed which will generate the seventh and eighth error message given in example 1 of section.
- This routine is used only if condensation is requested
- No implementation

---
XINTL(NPTS,X,DISTX)
- This routine calculates the initial distribution n(xi,0),
- A listing of the XINTL routine supplied with the code is given in figure 7
- The second integer in the common block AERSL1 is used to determine the functional form of the initial distribution.
- No implementation

---
Interpolation, integration and output routines

---
DISTW(ISPLIN,NVARM1,NPTS,WX,ZDIST)
- This routine determines the values of the “M” distribution given in eq[12], by interpolation from the values of the “M” distribution at the grid points.
- The array WX contains the “W” values given in eq[11] at which the values of the “M” distribution are to be computed and stored in the ZDIST array.
- ISPLIN is the user specified flag which determines the interpolation method
- NVARML is the number of grid points minus l and NPTS is the number of points in the WX array.
- The values of the “M” distribution, the conserved quantity of the aerosol x, and the “W” values at the grid points are stored in the common block AERSL2
- For ISPLIN equal to 0, 1 or 2, cubic, linear or logarithmic splines will be used

---
SETUP(ISPLIN,NEWSET,NVAR)
- This routine performs any preliminary calculations needed for interpolating the value of the “M” distribution
- ISPLIN is the flag which specifies the interpolation formula,
- NEWSET is the flag which indicates if a new set of grid points has been specified since the last call to SETUP and NVAR is the number of grid points.
- SETUP routine supplied with the code is used for determining the second derivatives of the distribution at the grid points for a cubic spline interpolation
- Figure 9

---
DERIVT(ISPLIN,NVAR,DERIV)
- This routine calculates the derivatives of the “M” distribution with respect to “W” at NVAR grid points and stores the derivatives in the array DERIV.
- This routine is required only if condensation is requested.

---
BLOCK DATA
- This data block stores the quadrature points and weight factors needed for an even point Gaussian-Legendre quadrature formula
- The number of quadrature points must be specified as an even number in this routine.

---
OUTPUT(ISTOP)
- This routine prints the results of a simulation at the times specified by the user in the input data cards.
- ISTOP is an error flag with the following meaning 0, 1, -1, -2

---
Convenience routines

---
CHECK(ISTOP)
- This routine checks the user input for obvious errors and prints an error message if any errors are encountered
- The routine will go through all error checks regardless of the number of errors and
  - ISTOP will be set to 0 if no errors are found
  - or to 1 if an error is found
If array dimensions are changed, the following variables in the data statement should be changed to the new dimensions

---
TOTAL(TOTALQ)
- This routine computes the effect of source and removal mechanisms on the first moment of the distribution.
- TOTAL should only be called if ISTOP=0 in the OUTPUT routine

---
CHKTBL(ISTOP)
This routine checks the interpolation for negative values of the distribution.

---
STEADY(TIME)
This routine computes the steady state cluster concentrations in the discrete regime.

---
Central routines

---
- Users should seldom need to be concerned with these routines
- MAIN: control program
- INPUT: reads input data
- COAGCF: stores values of coagulation and evaporation coefficients
- DIFFUN:calculates derivatives needed for O.D.E. package

---
Ordinary Differential Equation

---
Sandia`s O.D.E. package is used to integrate the set of ordinary differential equations

---
Section 5: Input data