        variables used by the program

    A(I)=for i=1 to nvar it is the value of the continuous
      distribution at the i-th grid point.
        for i=nvar+1 to nvart it is the number of particles at the discrete size
  i-nvar
    ABSERR=absolute integration error (see ode code write up)
    ADIF(I)=this array is used to transfer the a array to the ode package.
    ASAVE(I)=saved a array from last output time
    ALGXBA=ln(xb/xa)
    ATRY(I)=next iteration for the concentration of the i-th cluster,
      using the steady state approximation
    BESR(i,j)=coagulation coefficient times the jacobian for the i-th
      discrete cluster with a particle in the continuous regime such
      that a particle at the j-th grid point is formed
    BETADC(i,j)=the coagulation coefficient of the i-th cluster with
      the j-th grid point
    BETDSR(i)=storage array for cluster-cluster coagulation
      coefficients
    BOTTOM=lower limit of integration
    dadt(i)=the derivative of adif(i) with respect to time
    diag(i)=diagonal elements of tri-diagonal matrix
    distd=number distribution (number/cc)
    dists=surface area distribution (square cm/cc)
    distv=volume distribution (cc/cc)
    dmean=mean diameter (cm)
    evapr=total monomer evaporation rate from the continuous regime
    evpstr(i)=evaporation coefficient at the i-th grid point. for
      i=nvarp2 to nvart, this is the evaporation coefficient of the
      i-th cluster
    fact1a(i,j)=the i-th quadrature factor for the first term of the
      first coagulation integral for the j-th grid point
    fact1b(i,j)=the i-th quadrature factor for the second term of the
      first coagulation integral for the j-th grid point
    fact2(i,j)=the i-th quadrature factor for the second coagulation
      integral for the j-th grid point. for j=nvarp1 to nvart this is
      the quadrature factor for the scavenging of the (j-nvar)-th
      cluster by particles in the continuous regime
    facte1(i)=the i-th quadrature factor for the gain of monomer due
      to evaporation from the continuous regime
     facte3(i)=the i-th quadrature factor for evaporation from the
       continuous regime to form the largest discrete particle
     factor(i)=the i-th quadrature weight factor for integration over
       the entire continuous domain
    headng=character string for heading
    icase=the case number being solved
    icondn= 0=no condnesation/1=with condensation
    iflag=flag to ode, 1 indicates this is the first call
    igrid=number of grid points given
     iparm(i)=the i-th user supplied parameter
     iprnt=printer logical unit number
     iread=card reader logical unit number
    isetsw=output number to switch interpolation method
    isetup=flag to call setup before interpolating (0=no/1=yes)
    isplin=flag to indicate 0=cubic spline interpolation
        1=linear spline interpolation
        2=logarithmic interpolation
    ispswt=flag to call setup for switched interpolation method
      (0=no/1=yes)
 216 c* issflg=steady state flag, 0=do not use the steady state
 217 c* approximation, 1=use the steady state approximation for the
 218 c* discrete regime
 219 c* isstat=output number at which the steady state approximation is
 220 c* to be used. if zero do not use the s.s. approximation. if
 221 c* -1 print s.s. but do not use. if -2 switch to s.s. when
 222 c* specified error tolerances have been met
 223 c* istop=error flag, 1=error,0=no error,-1=correctable error,code
 224 c* will revert to previous output time,-2=print only discrete
 225 c* regime as determined from the steady state approximation
 226 c* iswtch=the output number for which the program is to
 227 c* switch interpolation methods
 228 c* itimdp=flag for time dependent coagulation and evaporation
 229 c* coefficients (0=time independent/1=time dependent)
 230 c* jprtim=the printing do-loop counter
 231 c* maxevp=the last grid point in the continuous regime for which
 232 c* evaporation is still included
 233 c* maxgdc(i)=maximum discrete cluster size that can coagulate with a
 234 c* particle in the continuous regime to form a particle at the i-th
 235 c* grid point
 236 c* maxsz=the largest discrete cluster that can coagulate with another
 237 c* discrete cluster to from the cluster of interest
 238 c* minw=smallest grid point for which the first coagulation integral
 239 c* is to be computed
 240 c* mxcase=maximum number of cases to solve. will default to one if
 241 c* less than or equal to zero
 242 c* ncremv=number of continuous removals
 243 c* ncsorc=number of continuous sources
 244 c* ndcls(i)=the discrete size number of the i-th grid point given in
 245 c* the continuous regime
 246 c* ndiscr=number of discrete sizes
 247 c* ndremv=number of discrete removals
 248 c* ndsorc=number of discrete sources
 249 c* nmulgv=number of discrete multiplets given in the continuous
 250 c* regime
 251 c* nmulp1=number of multiplets given plus one
 252 c* nmulp2=number of multiplets given plus two
 253 c* nmxvar=maximum number of grid points
 254 c* nprnt=number of outputs
 255 c* nptbet=number of interpolated points between grid points
 256 c* nquadp=number of quadrature points (must be an even number)
 257 c* nquad2=half the number of quadrature points
 258 c* ntroub=number of points at which distribution is negative
 259 c* nvar=number of variables in the continuous regime
 260 c* (equal to the number of grid points)
 261 c* nvarp1=nvar+1=number of variables plus one
 262 c* nvarp2=nvar+2=number of variables plus two
 263 c* nvart=total number of variables=nvar+ndiscr
 264 c* p(i)=storage array for the second derivative of m(w,t) with
 265 c* respect to w at the i+1 grid point. at the first and last grid
 266 c* point the second derivative is assumed to be zero.
 267 c* relerr=relative error (see ode code write up)
 268 c* scavng(i)=scavenging rate of the i-th cluster
 269 c* totalq=array containing the first moments of aerosol added
 270 c* to and removed from the continuous regime, and added to
 271 c* and removed from the discrete regime for each mechanism,
 272 c* respectively
 273 c* totnum=total number of particles/cc
 274 c* totsur=total surface area (square cm/cc)
 275 c* totvol=total volume of particles (cc/cc)
 276 c* tout(i)=the i-th output time
 277 c* sub(i)=sub-diagonal elements of tri-diagonal matrix
 278 c* super(i)=super-diagonal elements of tri-diagonal matrix
 279 c* txa=ln(2)/ln(xb/xa)= the w size of a particle produced when
 280 c* two of the smallest paticles of size w=0 coagulate
 281 c* upper=upper limit of integration
 282 c* w(i)=ln(x/xa)/ln(xb/xa) of the i-th grid point
 283 c* wbet(i)=the i-th w value interpolated between two grid points
 284 c* wd(i,j)=the w of a particle in the continuous regime, such that
 285 c* when it coagualtes with the i-th discrete cluster a particle of
 286 c* size w(j) is formed
 287 c* wmz1(i,j)=the w size of a particle which when it coagulates with a
 288 c* particle at the i-th quadrature point, a particle at the j-th
 289 c* grid point is formed
 290 c* wpls(i)=the w size of the i-th grid point plus a monomer
 291 c* x(i)=particle size at the i-th grid point
 292 c* xa=size of smallest particle
 293 c* xb=size of largest particle
 294 c* xbet=particle size of interpolated points between two grid points
 295 c* xboxa=xb/xa
 296 c* xtroub(i)=particle size array at which distribution is negative
 297 c* z(i)=the w size of the i-th quadrature point over the entire
 298 c* continuous regime
 299 c* zmass(i)=the particle size at the i-th quadrature point
 300 c* z1(i,j)=the i-th quadrature point for the first coagulation
 301 c* integral for the j-th grid point
 302 c* z2(i,j)=the i-th quadrature point for the second coagualtion
 303 c* integral for the j-th grid point

 157 C* VARIABLES USED BY THE PROGRAM
 158 C*
 159 C* A(I)=FOR I=1 TO NVAR IT IS THE VALUE OF THE CONTINUOUS
 160 C* DISTRIBUTION AT THE I-TH GRID POINT. FOR I=NVAR+1 TO NVART
 161 C* IT IS THE NUMBER OF PARTICLES AT THE DISCRETE SIZE I-NVAR
 162 C* ABSERR=ABSOLUTE INTEGRATION ERROR (SEE ODE CODE WRITE UP)
 163 C* ADIF(I)=THIS ARRAY IS USED TO TRANSFER THE A ARRAY TO THE ODE
 164 C* PACKAGE.
 165 C* ASAVE(I)=SAVED A ARRAY FROM LAST OUTPUT TIME
 166 C* ALGXBA=LN(XB/XA)
 167 C* ATRY(I)=NEXT ITERATION FOR THE CONCENTRATION OF THE I-TH CLUSTER,
 168 C* USING THE STEADY STATE APPROXIMATION
 169 C* BESR(I,J)=COAGULATION COEFFICIENT TIMES THE JACOBIAN FOR THE I-TH
 170 C* DISCRETE CLUSTER WITH A PARTICLE IN THE CONTINUOUS REGIME SUCH
 171 C* THAT A PARTICLE AT THE J-TH GRID POINT IS FORMED
 172 C* BETADC(I,J)=THE COAGULATION COEFFICIENT OF THE I-TH CLUSTER WITH
 173 C* THE J-TH GRID POINT
 174 C* BETDSR(I)=STORAGE ARRAY FOR CLUSTER-CLUSTER COAGULATION
 175 C* COEFFICIENTS
 176 C* BOTTOM=LOWER LIMIT OF INTEGRATION
 177 C* DADT(I)=THE DERIVATIVE OF ADIF(I) WITH RESPECT TO TIME
 178 C* DIAG(I)=DIAGONAL ELEMENTS OF TRI-DIAGONAL MATRIX
 179 C* DISTD=NUMBER DISTRIBUTION (NUMBER/CC)
 180 C* DISTS=SURFACE AREA DISTRIBUTION (SQUARE CM/CC)
 181 C* DISTV=VOLUME DISTRIBUTION (CC/CC)
 182 C* DMEAN=MEAN DIAMETER (CM)
 183 C* EVAPR=TOTAL MONOMER EVAPORATION RATE FROM THE CONTINUOUS REGIME
 184 C* EVPSTR(I)=EVAPORATION COEFFICIENT AT THE I-TH GRID POINT. FOR
 185 C* I=NVARP2 TO NVART, THIS IS THE EVAPORATION COEFFICIENT OF THE
 186 C* I-TH CLUSTER
 187 C* FACT1A(I,J)=THE I-TH QUADRATURE FACTOR FOR THE FIRST TERM OF THE
 188 C* FIRST COAGULATION INTEGRAL FOR THE J-TH GRID POINT
 189 C* FACT1B(I,J)=THE I-TH QUADRATURE FACTOR FOR THE SECOND TERM OF THE
 190 C* FIRST COAGULATION INTEGRAL FOR THE J-TH GRID POINT
 191 C* FACT2(I,J)=THE I-TH QUADRATURE FACTOR FOR THE SECOND COAGULATION
 192 C* INTEGRAL FOR THE J-TH GRID POINT. FOR J=NVARP1 TO NVART THIS IS
 193 C* THE QUADRATURE FACTOR FOR THE SCAVENGING OF THE (J-NVAR)-TH
 194 C* CLUSTER BY PARTICLES IN THE CONTINUOUS REGIME
 195 C* FACTE1(I)=THE I-TH QUADRATURE FACTOR FOR THE GAIN OF MONOMER DUE
 196 C* TO EVAPORATION FROM THE CONTINUOUS REGIME
 197 C* FACTE3(I)=THE I-TH QUADRATURE FACTOR FOR EVAPORATION FROM THE
 198 C* CONTINUOUS REGIME TO FORM THE LARGEST DISCRETE PARTICLE
 199 C* FACTOR(I)=THE I-TH QUADRATURE WEIGHT FACTOR FOR INTEGRATION OVER
 200 C* THE ENTIRE CONTINUOUS DOMAIN
 201 C* HEADNG=CHARACTER STRING FOR HEADING
 202 C* ICASE=THE CASE NUMBER BEING SOLVED
 203 C* ICONDN= 0=NO CONDNESATION/1=WITH CONDENSATION
 204 C* IFLAG=FLAG TO ODE, 1 INDICATES THIS IS THE FIRST CALL
 205 C* IGRID=NUMBER OF GRID POINTS GIVEN
 206 C* IPARM(I)=THE I-TH USER SUPPLIED PARAMETER
 207 C* IPRNT=PRINTER LOGICAL UNIT NUMBER
 208 C* IREAD=CARD READER LOGICAL UNIT NUMBER
 209 C* ISETSW=OUTPUT NUMBER TO SWITCH INTERPOLATION METHOD
 210 C* ISETUP=FLAG TO CALL SETUP BEFORE INTERPOLATING (0=NO/1=YES)
 211 C* ISPLIN=FLAG TO INDICATE 0=CUBIC SPLINE INTERPOLATION
 212 C* 1=LINEAR SPLINE INTERPOLATION
 213 C* 2=LOGARITHMIC INTERPOLATION
 214 C* ISPSWT=FLAG TO CALL SETUP FOR SWITCHED INTERPOLATION METHOD
 215 C* (0=NO/1=YES)
 216 C* ISSFLG=STEADY STATE FLAG, 0=DO NOT USE THE STEADY STATE
 217 C* APPROXIMATION, 1=USE THE STEADY STATE APPROXIMATION FOR THE
 218 C* DISCRETE REGIME
 219 C* ISSTAT=OUTPUT NUMBER AT WHICH THE STEADY STATE APPROXIMATION IS
 220 C* TO BE USED. IF ZERO DO NOT USE THE S.S. APPROXIMATION. IF
 221 C* -1 PRINT S.S. BUT DO NOT USE. IF -2 SWITCH TO S.S. WHEN
 222 C* SPECIFIED ERROR TOLERANCES HAVE BEEN MET
 223 C* ISTOP=ERROR FLAG, 1=ERROR,0=NO ERROR,-1=CORRECTABLE ERROR,CODE
 224 C* WILL REVERT TO PREVIOUS OUTPUT TIME,-2=PRINT ONLY DISCRETE
 225 C* REGIME AS DETERMINED FROM THE STEADY STATE APPROXIMATION
 226 C* ISWTCH=THE OUTPUT NUMBER FOR WHICH THE PROGRAM IS TO
 227 C* SWITCH INTERPOLATION METHODS
 228 C* ITIMDP=FLAG FOR TIME DEPENDENT COAGULATION AND EVAPORATION
 229 C* COEFFICIENTS (0=TIME INDEPENDENT/1=TIME DEPENDENT)
 230 C* JPRTIM=THE PRINTING DO-LOOP COUNTER
 231 C* MAXEVP=THE LAST GRID POINT IN THE CONTINUOUS REGIME FOR WHICH
 232 C* EVAPORATION IS STILL INCLUDED
 233 C* MAXGDC(I)=MAXIMUM DISCRETE CLUSTER SIZE THAT CAN COAGULATE WITH A
 234 C* PARTICLE IN THE CONTINUOUS REGIME TO FORM A PARTICLE AT THE I-TH
 235 C* GRID POINT
 236 C* MAXSZ=THE LARGEST DISCRETE CLUSTER THAT CAN COAGULATE WITH ANOTHER
 237 C* DISCRETE CLUSTER TO FROM THE CLUSTER OF INTEREST
 238 C* MINW=SMALLEST GRID POINT FOR WHICH THE FIRST COAGULATION INTEGRAL
 239 C* IS TO BE COMPUTED
 240 C* MXCASE=MAXIMUM NUMBER OF CASES TO SOLVE. WILL DEFAULT TO ONE IF
 241 C* LESS THAN OR EQUAL TO ZERO
 242 C* NCREMV=NUMBER OF CONTINUOUS REMOVALS
 243 C* NCSORC=NUMBER OF CONTINUOUS SOURCES
 244 C* NDCLS(I)=THE DISCRETE SIZE NUMBER OF THE I-TH GRID POINT GIVEN IN
 245 C* THE CONTINUOUS REGIME
    NDISCR=NUMBER OF DISCRETE SIZES
 247 C* NDREMV=NUMBER OF DISCRETE REMOVALS
 248 C* NDSORC=NUMBER OF DISCRETE SOURCES
 249 C* NMULGV=NUMBER OF DISCRETE MULTIPLETS GIVEN IN THE CONTINUOUS
 250 C* REGIME
 251 C* NMULP1=NUMBER OF MULTIPLETS GIVEN PLUS ONE
 252 C* NMULP2=NUMBER OF MULTIPLETS GIVEN PLUS TWO
 253 C* NMXVAR=MAXIMUM NUMBER OF GRID POINTS
 254 C* NPRNT=NUMBER OF OUTPUTS
 255 C* NPTBET=NUMBER OF INTERPOLATED POINTS BETWEEN GRID POINTS
 256 C* NQUADP=NUMBER OF QUADRATURE POINTS (MUST BE AN EVEN NUMBER)
 257 C* NQUAD2=HALF THE NUMBER OF QUADRATURE POINTS
 258 C* NTROUB=NUMBER OF POINTS AT WHICH DISTRIBUTION IS NEGATIVE
    NVAR=NUMBER OF VARIABLES IN THE CONTINUOUS REGIME
        (EQUAL TO THE NUMBER OF GRID POINTS)
    NVARP1=NVAR+1=NUMBER OF VARIABLES PLUS ONE
    NVARP2=NVAR+2=NUMBER OF VARIABLES PLUS TWO
    NVART=TOTAL NUMBER OF VARIABLES=NVAR+NDISCR
    P(I)=STORAGE ARRAY FOR THE SECOND DERIVATIVE OF M(W,T) WITH
 265 C* RESPECT TO W AT THE I+1 GRID POINT. AT THE FIRST AND LAST GRID
 266 C* POINT THE SECOND DERIVATIVE IS ASSUMED TO BE ZERO.
 267 C* RELERR=RELATIVE ERROR (SEE ODE CODE WRITE UP)
 268 C* SCAVNG(I)=SCAVENGING RATE OF THE I-TH CLUSTER
 269 C* TOTALQ=ARRAY CONTAINING THE FIRST MOMENTS OF AEROSOL ADDED
 270 C* TO AND REMOVED FROM THE CONTINUOUS REGIME, AND ADDED TO
 271 C* AND REMOVED FROM THE DISCRETE REGIME FOR EACH MECHANISM,
 272 C* RESPECTIVELY
 273 C* TOTNUM=TOTAL NUMBER OF PARTICLES/CC
 274 C* TOTSUR=TOTAL SURFACE AREA (SQUARE CM/CC)
 275 C* TOTVOL=TOTAL VOLUME OF PARTICLES (CC/CC)
 276 C* TOUT(I)=THE I-TH OUTPUT TIME
 277 C* SUB(I)=SUB-DIAGONAL ELEMENTS OF TRI-DIAGONAL MATRIX
 278 C* SUPER(I)=SUPER-DIAGONAL ELEMENTS OF TRI-DIAGONAL MATRIX
 279 C* TXA=LN(2)/LN(XB/XA)= THE W SIZE OF A PARTICLE PRODUCED WHEN
 280 C* TWO OF THE SMALLEST PATICLES OF SIZE W=0 COAGULATE
 281 C* UPPER=UPPER LIMIT OF INTEGRATION
 282 C* W(I)=LN(X/XA)/LN(XB/XA) OF THE I-TH GRID POINT
 283 C* WBET(I)=THE I-TH W VALUE INTERPOLATED BETWEEN TWO GRID POINTS
 284 C* WD(I,J)=THE W OF A PARTICLE IN THE CONTINUOUS REGIME, SUCH THAT
 285 C* WHEN IT COAGUALTES WITH THE I-TH DISCRETE CLUSTER A PARTICLE OF
 286 C* SIZE W(J) IS FORMED
 287 C* WMZ1(I,J)=THE W SIZE OF A PARTICLE WHICH WHEN IT COAGULATES WITH A
 288 C* PARTICLE AT THE I-TH QUADRATURE POINT, A PARTICLE AT THE J-TH
 289 C* GRID POINT IS FORMED
 290 C* WPLS(I)=THE W SIZE OF THE I-TH GRID POINT PLUS A MONOMER
 291 C* X(I)=PARTICLE SIZE AT THE I-TH GRID POINT
 292 C* XA=SIZE OF SMALLEST PARTICLE
 293 C* XB=SIZE OF LARGEST PARTICLE
 294 C* XBET=PARTICLE SIZE OF INTERPOLATED POINTS BETWEEN TWO GRID POINTS
 295 C* XBOXA=XB/XA
 296 C* XTROUB(I)=PARTICLE SIZE ARRAY AT WHICH DISTRIBUTION IS NEGATIVE
 297 C* Z(I)=THE W SIZE OF THE I-TH QUADRATURE POINT OVER THE ENTIRE
 298 C* CONTINUOUS REGIME
 299 C* ZMASS(I)=THE PARTICLE SIZE AT THE I-TH QUADRATURE POINT
 300 C* Z1(I,J)=THE I-TH QUADRATURE POINT FOR THE FIRST COAGULATION
 301 C* INTEGRAL FOR THE J-TH GRID POINT
 302 C* Z2(I,J)=THE I-TH QUADRATURE POINT FOR THE SECOND COAGUALTION
 303 C* INTEGRAL FOR THE J-TH GRID POINT